## Slide 1
🍫 CHOCOLATE FACTORY
Facilities Planning & Layout Design
Industrial Engineering Project
Supervised by: Dr. Aziz Ezzat
Presented by: Shahd Elsanet | Abdelrahman Hatem

## Slide 2
TABLE OF CONTENTS
01
Introduction
02
Product Analysis
03
Process Analysis
04
Equipment Analysis
05
Machine Dimensions
06
Preliminary Layout
07
Fabrication Department (Preliminary)
08
Activity Relationship Chart
09
Activity Relationship Diagram
10
From-To Chart
11
Workstations Total Area
12
Fabrication Department Layout
13
Line Balancing – Welding/Enrobing Area
14
Line Balancing – Assembly/Packaging Area

## Slide 3
1. INTRODUCTION
1
Project Objective:
Design an efficient factory layout for a chocolate manufacturing plant to maximise throughput and minimise material handling costs.
2
Scope:
Covers product analysis, process flow, equipment selection, workstation sizing, and final plant layout for a medium-scale chocolate factory.
3
Products:
The factory produces three main lines: Milk Chocolate Bars, Dark Chocolate Truffles, and Chocolate-Coated Wafers.
4
Production Volume:
Target capacity: 5,000 kg/day across all product lines, with a planned 8-hour single-shift operation (480 min/day).
5
Methodology:
Systematic Layout Planning (SLP) is applied — starting from activity relationships through final optimised layout selection.
6
Design Goals:
Achieve ≥85% line efficiency, <50 m average travel distance between adjacent departments, and full GMP/food-safety compliance.

## Slide 4
2. PRODUCT ANALYSIS
Milk Chocolate Bar
Dimensions:
150 × 75 × 10 mm
Unit Weight:
100 g/bar
Daily Volume:
2,000 kg/day
Key Ingredients:
Cocoa mass, milk powder, sugar, cocoa butter, soy lecithin
Packaging:
Aluminium foil wrap + printed paper sleeve
Dark Chocolate Truffle
Dimensions:
Ø 25 mm × 22 mm
Unit Weight:
12 g/piece
Daily Volume:
1,500 kg/day
Key Ingredients:
70% cocoa mass, fresh cream, butter, sugar, vanilla extract
Packaging:
Individual gold-foil wrap, boxed 12 pcs per gift box
Chocolate-Coated Wafer
Dimensions:
120 × 30 × 15 mm
Unit Weight:
45 g/bar
Daily Volume:
1,500 kg/day
Key Ingredients:
Wheat flour, milk-choc coating, cocoa butter, cream filling
Packaging:
Flow-wrap plastic with tamper-evident seal

## Slide 7
3. PROCESS ANALYSIS
01 Raw Material Receiving & QC
Cocoa beans, sugar, milk powder, cocoa butter received & sampled for quality specs
02 Mixing & Blending
⏱ 45 min
Ingredients blended in jacketed vessels at 40–50 °C; moisture controlled
03 Conching
⏱ 12 hrs
Continuous kneading develops flavour, reduces viscosity, smooth texture
04 Tempering
⏱ 30 min
Controlled cycle 50°C→27°C→31°C; stable β-crystal cocoa butter formation
05 Moulding / Enrobing
⏱ 20 min
Bars cast in moulds; wafers coated via enrobing belt at 31 °C
06 Cooling Tunnel
⏱ 15 min
Conveyor through 10–12 °C tunnel; chocolate sets and contracts for demoulding
07 Packaging & Labelling
⏱ 5 min
Automated wrap, seal, date-code, allergen label and weight check
08 Finished Goods Storage
Cold store at 18 °C, 50% RH; FIFO stock rotation before dispatch

## Slide 9
4. EQUIPMENT ANALYSIS
Equipment
Qty
Capacity
Power (kW)
Dimensions (L×W×H m)
Mixing & Blending Vessel
2
500 kg/batch
15
2.0 × 1.5 × 2.2
Conching Machine
3
1,000 kg/batch
45
4.0 × 2.0 × 1.8
Tempering Machine
2
800 kg/hr
22
3.5 × 1.2 × 1.5
Bar Moulding Line
1
2,000 bars/hr
35
8.0 × 1.0 × 1.6
Chocolate Enrober
1
300 kg/hr
18
5.0 × 1.5 × 1.4
Cooling Tunnel
2
500 kg/hr ea.
12
10.0 × 1.2 × 1.5
Flow-Wrap Packaging Machine
3
120 pcs/min
8
3.0 × 1.0 × 1.5
Truffle Depositor
1
150 kg/hr
10
2.5 × 1.0 × 1.6
Foil Wrapping Machine
2
200 pcs/min
7
2.0 × 0.8 × 1.4
QC Checkweigher
3
Inline
1
1.0 × 0.6 × 1.2

## Slide 10
5. MACHINE DIMENSIONS — Top-View Footprints
Scaled floor footprints (scale: 1 grid unit ≈ 1 m). Each box shows L × W (m) and unit area.
Mixing Vessel
(×2)
2×1.5 m
2 m →
Conching
(×3)
4×2 m
4 m →
Tempering
(×2)
3.5×1.2 m
3.5 m →
Moulding Line
(×1)
8×1 m
8 m →
Enrober
(×1)
5×1.5 m
5 m →
Cooling Tunnel
(×2)
10×1.2 m
10 m →
Packaging
(×3)
3×1 m
3 m →
Footprint Summary
Mixing Vessel (×2)
2.0×1.5 = 3.0 m²
Conching Machine (×3)
4.0×2.0 = 8.0 m²
Tempering (×2)
3.5×1.2 = 4.2 m²
Moulding Line (×1)
8.0×1.0 = 8.0 m²
Enrober (×1)
5.0×1.5 = 7.5 m²
Cooling Tunnel (×2)
10.0×1.2 = 12.0 m²
Packaging (×3)
3.0×1.0 = 3.0 m²
Total Equipment Area
≈ 45.7 m²

## Slide 11
6. PRELIMINARY LAYOUT — Alternatives Evaluation
Alt. A — Linear Flow
All departments in a straight production line. Simplest material flow, easiest supervision.
✔ Advantages
• Simple, single-direction flow
• Easy material tracking
• Low WIP accumulation
• Straightforward supervision
✖ Disadvantages
• Very high building length requirement
• Poor space utilisation
• Receiving & dispatch far apart
Alt. B — U-Shape ✓ CHOSEN
U-shaped flow returns dispatch area near receiving. Best material handling efficiency and compact footprint.
✔ Advantages
• Compact layout (~850 m²)
• Receiving & dispatch adjacent
• Flexible multi-skilled workforce
• Best material handling efficiency
✖ Disadvantages
• Slightly complex flow supervision
• Higher utility piping cost
Alt. C — L-Shape
L-shaped flow splits packaging wing from production. Reduces congestion at packaging end.
✔ Advantages
• Good future expansion space
• Packaging segregated from production
✖ Disadvantages
• Longer average material travel
• Requires two supervision zones
• Higher inter-department distances

## Slide 12
7. FABRICATION DEPARTMENT — Preliminary Layout
Preliminary zone allocations before detailed SLP. All dimensions in metres.
RAW MATERIAL
STORE
24 m²
MIXING
& BLENDING
20 m²
CONCHING
24 m²
TEMPERING
18 m²
MOULDING &
ENROBING
30 m²
COOLING
TUNNEL
24 m²
PACKAGING
LINE
24 m²
QC
LABORATORY
24 m²
UTILITIES
& SERVICES
16 m²
FINISHED GOODS
WAREHOUSE
96 m²
DISPATCH
BAY
—
Total Fabrication Dept Area: ≈ 300 m² | Building footprint: 30 m × 10 m (preliminary)

## Slide 13
8. ACTIVITY RELATIONSHIP CHART
A
= Absolutely Necessary
E
= Especially Important
I
= Important
O
= Ordinary Closeness
U
= Unimportant
X
= Undesirable
Receiving
Mixing
Conching
Tempering
Moulding
Cooling
Packaging
Dispatch
Receiving
—
A
U
U
U
U
U
E
Mixing
—
A
U
U
U
U
U
Conching
—
A
U
U
U
U
Tempering
—
A
E
U
U
Moulding
—
A
U
U
Cooling
—
A
U
Packaging
—
A
Dispatch
—

## Slide 14
9. ACTIVITY RELATIONSHIP DIAGRAM
Receiving
Mixing
Conching
Tempering
Moulding
Cooling
Packaging
Dispatch
QC Lab
Utilities
A – Absolutely Nec.
E – Especially Imp.
I – Important
Flow: Receiving → Mixing → Conching → Tempering → Moulding → Cooling → Packaging → Dispatch
(U-shaped loop; QC Lab and Utilities support all stations)

## Slide 15
10. FROM-TO CHART — Material Flow (kg/day)
Receivi
Mixing
Conchin
Temperi
Mouldin
Cooling
Packagi
Dispatc
Receivi
—
5,000
Mixing
—
5,000
Conchin
—
5,000
Temperi
—
3,500
Mouldin
—
5,000
Cooling
—
5,000
Packagi
—
5,000
Dispatc
—
★ Zero backflow — all material moves forward in the production sequence. Peak throughput: 5,000 kg/day.

## Slide 16
11. WORKSTATIONS TOTAL AREA
Department / Workstation
Qty
Dimensions (m)
Unit Area (m²)
Space Factor
Total Area (m²)
Receiving & Inspection
1
8.0 × 6.0
48.0
1.5
72.0
Mixing & Blending
2
5.0 × 4.0
20.0
2.0
80.0
Conching
3
6.0 × 4.0
24.0
2.0
144.0
Tempering
2
5.0 × 3.0
15.0
2.0
60.0
Moulding / Enrobing
2
10.0 × 3.0
30.0
1.5
90.0
Cooling Tunnel
2
12.0 × 2.0
24.0
1.5
72.0
Packaging Assembly
3
5.0 × 3.0
15.0
2.0
90.0
QC Laboratory
1
6.0 × 4.0
24.0
1.0
24.0
Finished Goods Warehouse
1
12.0 × 8.0
96.0
1.2
115.2
Utilities / Boiler Room
1
6.0 × 4.0
24.0
1.0
24.0
TOTAL
771.2 m²

## Slide 17
12. FABRICATION DEPARTMENT — Final Layout (U-Shape)
Chosen layout: U-Shape (Alt. B). Scale: approx. 1 cm = 3 m. Total building: 30 m × 28 m ≈ 840 m².
RECEIVING
& INSPECTION
72 m²
MIXING
& BLENDING
80 m²
CONCHING
144 m²
TEMPERING
60 m²
MOULDING
& ENROBING
90 m²
COOLING
TUNNEL
72 m²
PACKAGING
ASSEMBLY
90 m²
QC
LAB
24 m²
UTILITIES
& SERVICES
24 m²
FINISHED
GOODS STORE
115 m²
DISPATCH BAY
→ Top arm (Production) ↓ Right (Cooling) ← Bottom arm (Packaging → Dispatch) ↑ Left (Storage)

## Slide 18
13. LINE BALANCING — Moulding / Enrobing Area
Demand Rate
5,000 kg/day
Working Time
480 min/day
Cycle Time
CT = 0.096 min/kg
Theoretical N
N = Σti / CT
Task
Description
Time (min/100kg)
Pred.
Station
A
Tempering machine feed
12.0
—
WS-1
B
Mould filling / depositing
8.5
A
WS-1
C
Vibration (air bubble removal)
4.0
B
WS-1
D
Cooling tunnel pass
15.0
C
WS-2
E
Demoulding / extraction
6.0
D
WS-2
F
Enrober chocolate coating
9.5
E
WS-2
G
Post-enrobe cooling pass
12.0
F
WS-3
H
Visual QC inspection
3.5
G
WS-3
I
Checkweigher inline
2.0
H
WS-3
J
Rejection & rework feed
3.0
I
WS-3
Summary
Σ Task Times
76.5 min
# Stations
3 WS
Bottleneck
WS-2: 33 min
Efficiency
(76.5/99)
= 77.3%

## Slide 19
14. LINE BALANCING — Packaging / Assembly Area
Output Target
5,000 kg/day
Working Time
480 min/day
Cycle Time
CT = 0.096 min/kg
Workstations
4 WS assigned
ID
Task Description
Time (min/batch)
Pred.
Workstation
P1
Unwrap / de-nest product
2.5
—
WS-1
P2
Primary wrap (foil / flow-pack)
5.0
P1
WS-1
P3
Label & date-code application
3.0
P2
WS-1
P4
Checkweigher pass
1.5
P3
WS-2
P5
Metal detector pass
1.5
P4
WS-2
P6
Vision QC (colour & shape)
2.5
P5
WS-2
P7
Carton erecting & loading
6.0
P6
WS-3
P8
Carton sealing & coding
3.5
P7
WS-3
P9
Case / shipper packing
5.5
P8
WS-4
P10
Palletising & stretch-wrap
4.0
P9
WS-4
WS Efficiency
WS-1
87.5%
Σ=10.5 min
WS-2
45.8%
Σ=5.5 min
WS-3
79.2%
Σ=9.5 min
WS-4
79.2%
Σ=9.5 min
Line Efficiency
= 35 / 48 = 72.9%
Bottleneck: WS-1
(Primary Wrapping)

## Slide 20
CONCLUSIONS & RECOMMENDATIONS
01
U-Shape Layout Selected
Achieves minimum average travel distance of 42 m between adjacent departments with 100% forward-only material flow.
02
Total Plant Area: 840 m²
Building: 30 m × 28 m. Equipment footprint 45.7 m², total workstation area 771.2 m² including clearances and aisles.
03
Moulding/Enrobing Line Efficiency: 77.3%
3 workstations; bottleneck at WS-2 (cooling + demoulding). Recommend adding one conching machine to balance WS-2.
04
Packaging Line Efficiency: 72.9%
4 workstations; bottleneck at WS-1. Recommend a second flow-wrap machine to reduce wrapping cycle time.
05
Quality & Compliance
QC lab centrally located with access to all production lines. Metal detectors and checkweighers at packaging stage for GMP compliance.
06
Future Expansion
U-shape allows +30% capacity by extending the top arm eastward without disrupting existing flow. Utilities zone pre-sized for expansion.
Chocolate Factory — Facilities Planning Project | Dr. Aziz Ezzat | Shahd Elsanet & Abdelrahman Hatem